## Slide 1
Rework and Re-inspection
Use As Is
Scrap
Conditional Release
Discrepancy/Non-Conformance Identified
User completes NCMR, marks product, and forwards to QA for segregation
QA identifies MRB requirements and calls MRB meeting
MRB meets, reviews non-conformance and documents disposition and suggested corrective/preventive action
MRB Disposition?
 | Non-Conforming Material Process Flowchart
Non-Conforming Material Process Flowchart Confidential & Proprietary
Document Number: QA-026 Page 1 of 4
Version Number: 000
Reject

## Slide 2
Yes
 | Non-Conforming Material Process Flowchart
Non-Conforming Material Process Flowchart Confidential & Proprietary
Document Number: QA-026 Page 2 of 4
Version Number: 000
Use As Is
Conditional Release
QA modifies product labeling to reflect disposition and forwards product to appropriate location
NCMR Final Review
Rework
Reject
Scrap
Appropriate department performs rework
QA performs inspection of rework
Acceptable?
Return to MRB Meeting
QA modifies product labeling to reflect disposition and forwards product to Purchasing for return to supplier
NCMR Final Review
Product destroyed and/or disposed of in an appropriate manner including all labeling
No
CAPA Required?
A copy of the NCMR is used to initiate a SCPAP to include in return shipment to supplier
Corrective and Preventive Action Plans Policy and Procedure
Yes
No

## Slide 3
 | Non-Conforming Material Process Flowchart
QA reviews NCMR for accuracy and completeness, any issues resolved
NCMR information entered into tracking records and original and all attachments filed
CAPA Required?
A copy of the NCMR is used to initiate a CPAP or SCPAP as necessary
Corrective and Preventive Action Plans Policy and Procedure
No
Yes
NCMR Final Review
Non-Conforming Material Process Flowchart Confidential & Proprietary
Document Number: QA-026 Page 3 of 4
Version Number: 000

## Slide 4
 | Non-Conforming Material Process Flowchart
Document Revision History
Change Order Number: | Version Number: | Description of Change: | Date: | Updated by:
CC-100526-01 | 000 | New Document | 05/28/10 | A.M.M.
Non-Conforming Material Process Flowchart Confidential & Proprietary
Document Number: QA-026 Page 4 of 4
Version Number: 000